CO2412
Computational Thinking
Formal verification
Performance and efficiency

---
Design by contract
Specify
Function specification – what it should do
Non-functional specification – how well it should do it
Design
Select appropriate algorithms and data structures
Consider effectiveness/correctness – does it do what it is supposed to?
Consider efficiency
Size
Speed
Implement
Create solution at low level
“contracts” between specifier, designer, and programmer
We need a way of specifying algorithms and their outcomes

---
Design by contract
Specify
Function specification – what it should do
Non-functional specification – how well it should do it
Design
Select appropriate algorithms and data structures
Consider effectiveness/correctness – does it do what it is supposed to?
Consider efficiency
Size
Speed
Implement
Create solution at low level
Evaluate
Debug, assess for syntactic & semantic correctness
Check performance (i.e., resource requirements)
“contracts” between specifier, designer, and programmer
We need a way of evaluating algorithms and their outcomes

---
Formal verification

---
Verification, validation, and testing
Verification: Proof that the developed product complies with its specification.
Where possible, provide a rigorous logical/mathematical proof; alternatively, provide documents following agreed standards/procedures.
develop-
ment
systematic
deploy-
ment
empirical
Testing: Use-case driven evaluation of the final (or alpha, or beta) product.
The considered use cases should be representative.
They should be as unrelated as possible to any concrete scenarios considered during development, including the validation process.

---
Verification, validation, and testing
Verification: Proof that the developed product complies with its specification.
Where possible, provide a rigorous logical/mathematical proof; alternatively, provide documents following agreed standards/procedures.
develop-
ment
systematic
developer-
driven
deploy-
ment
empirical
user-driven
Testing: Use-case driven evaluation of the final (or alpha, or beta) product.
The considered use cases should be representative.
They should be as unrelated as possible to any concrete scenarios considered during development, including the validation process.
Ideally, conducted by prospective users; if unavailable, “play the user.”

---
Verification, validation, and testing
Verification: Proof that the developed product complies with its specification.
Where possible, provide a rigorous logical/mathematical proof; alternatively, provide documents following agreed standards/procedures.
Validation: Empirical evaluation to what extent user the requirements are met.
All requirements need to be covered and demonstrated at least once.
Ideally, requirements are not identical with the specification. They should be user-oriented; e.g., epics and user stories in a requirements analysis from agile software engineering. Feedback from users is needed.
Testing: Use-case driven evaluation of the final (or alpha, or beta) product.
The considered use cases should be representative.
They should be as unrelated as possible to any concrete scenarios considered during development, including the validation process.
Ideally, conducted by prospective users; if unavailable, “play the user.”

---
Verification, validation, and testing
Verification: Proof that the developed product complies with its specification.
Where possible, provide a rigorous logical/mathematical proof; alternatively, provide documents following agreed standards/procedures.
Remark
Verification always has the meaning that something is demon-
strated to be true, particularly by logical reasoning. Validation and testing have many meanings to different communities; the
distinction here is common in AI (e.g., validation set vs. test set).
Validation: Empirical evaluation to what extent user the requirements are met.
All requirements need to be covered and demonstrated at least once.
Ideally, requirements are not identical with the specification. They should be user-oriented; e.g., epics and user stories in a requirements analysis from agile software engineering. Feedback from users is needed.
Testing: Use-case driven evaluation of the final (or alpha, or beta) product.
The considered use cases should be representative.
They should be as unrelated as possible to any concrete scenarios considered during development, including the validation process.
Ideally, conducted by prospective users; if unavailable, “play the user.”

---
Verification, validation, and testing
Verification: Proof that the developed product complies with its specification.
Where possible, provide a rigorous logical/mathematical proof; alternatively, provide documents following agreed standards/procedures.
Note
The above is what we mean by formal verification.
There can be no verification without a specification.
It can be done by humans, using code or pseudocode.
Validation: Empirical evaluation to what extent user the requirements are met.
All requirements need to be covered and demonstrated at least once.
Ideally, requirements are not identical with the specification. They should be user-oriented; e.g., epics and user stories in a requirements analysis from agile software engineering. Feedback from users is needed.
Testing: Use-case driven evaluation of the final (or alpha, or beta) product.
The considered use cases should be representative.
They should be as unrelated as possible to any concrete scenarios considered during development, including the validation process.
Ideally, conducted by prospective users; if unavailable, “play the user.”

---
Verification, validation, and testing
Verification: Proof that the developed product complies with its specification.
Where possible, provide a rigorous logical/mathematical proof; alternatively, provide documents following agreed standards/procedures.
Note
The above is what we mean by formal verification.
There can be no verification without a specification.
It can be done by humans, using code or pseudocode.
It can also be done computationally (automated verification); in that case, either the programming language must be restricted severely, or it is only a model of the program that can be verified.
The latter is known as model checking. It is limited by the accuracy and extent of the information provided in the model.
Validation: Empirical evaluation to what extent user the requirements are met.
All requirements need to be covered and demonstrated at least once.
Ideally, requirements are not identical with the specification. They should be user-oriented; e.g., epics and user stories in a requirements analysis from agile software engineering. Feedback from users is needed.
Testing: Use-case driven evaluation of the final (or alpha, or beta) product.
The considered use cases should be representative.
They should be as unrelated as possible to any concrete scenarios considered during development, including the validation process.
Ideally, conducted by prospective users; if unavailable, “play the user.”

---
Program flow graphs1
1F. Nielson, H. Riis Nielson, C. Hankin, Principles of Program Analysis, Heidelberg: Springer, 2005.

---
Preconditions and postconditions
For purposes of formal analysis, the program flow is analysed step by step, e.g., at the instruction (statement) level, at the level of blocks of code that form a coherent unit, or at the level of functions or methods.
Precondition: State of the program at a point directly before the considered unit. This may include assumptions taken from the design contract or specification.
Postcondition: State of the program at a point directly after the considered unit, assuming that the precondition was fulfilled at the point directly before it.
Example
As part of a development project, we need a function grtfrac(x, y) that takes two floating-point arguments and returns the one with the greater fractional part; e.g., grtfrac(2.7, 3.6) is to return 2.7, because “.7” is greater than “.6”. In design by contract, the caller, not the called method needs to guarantee the precondition.

---
Preconditions and postconditions
For purposes of formal analysis, the program flow is analysed step by step, e.g., at the instruction (statement) level, at the level of blocks of code that form a coherent unit, or at the level of functions or methods.
Precondition: State of the program at a point directly before the considered unit. This may include assumptions taken from the design contract or specification.
Postcondition: State of the program at a point directly after the considered unit, assuming that the precondition was fulfilled at the point directly before it.
Example
As part of a development project, we need a function grtfrac(x, y) that takes two floating-point arguments and returns the one with the greater fractional part; e.g., grtfrac(2.7, 3.6) is to return 2.7, because “.7” is greater than “.6”. In design by contract, the caller, not the called method needs to guarantee the precondition.

---
Preconditions and postconditions
For purposes of formal analysis, the program flow is analysed step by step, e.g., at the instruction (statement) level, at the level of blocks of code that form a coherent unit, or at the level of functions or methods.
Precondition: State of the program at a point directly before the considered unit. This may include assumptions taken from the design contract or specification.
Postcondition: State of the program at a point directly after the considered unit, assuming that the precondition was fulfilled at the point directly before it.
Example
As part of a development project, we need a function grtfrac(x, y) that takes two floating-point arguments and returns the one with the greater fractional part; e.g., grtfrac(–2.7, –1.8) is to return –2.7, because “.3” (or –0.7) is greater than “.2” (or –0.8).

---
Preconditions and postconditions
def grtfrac(x, y):
    if (x - x//1) > (y - y//1):
        return x
    else:
        return y
true
false
Example
As part of a development project, we need a function grtfrac(x, y) that takes two floating-point arguments and returns the one with the greater fractional part; e.g., grtfrac(2.7, 3.6) is to return 2.7, because “.7” is greater than “.6”.
if (x - x//1) > (y - y//1):
return x
return y

---
Preconditions and postconditions
initial state S0
def grtfrac(x, y):
    if (x - x//1) > (y - y//1):
        return x
    else:
        return y
true
false
S1
S2
final state S3
final state S4
Example
As part of a development project, we need a function grtfrac(x, y) that takes two floating-point arguments and returns the one with the greater fractional part; e.g., grtfrac(2.7, 3.6) is to return 2.7, because “.7” is greater than “.6”.
if (x - x//1) > (y - y//1):
return x
return y

---
Preconditions and postconditions
initial state S0
def grtfrac(x, y):
    if (x - x//1) > (y - y//1):
        return x
    else:
        return y
transitions S0 → S1, S2
true
false
S1
S2
transition S2 → S4
transition S1 → S3
final state S3
final state S4
Example
As part of a development project, we need a function grtfrac(x, y) that takes two floating-point arguments and returns the one with the greater fractional part; e.g., grtfrac(2.7, 3.6) is to return 2.7, because “.7” is greater than “.6”.
if (x - x//1) > (y - y//1):
return x
return y

---
Preconditions and postconditions
initial state S0
def grtfrac(x, y):
    if (x - x//1) > (y - y//1):
        return x
    else:
        return y
transitions S0 → S1, S2
true
false
S1
S2
transition S2 → S4
transition S1 → S3
final state S4
final state S3
Note
Consider the statement “return x” from transition S1 → S3:
The execution state S1 is the precondition of S1 → S3.
The execution state S3 is the postcondition of S1 → S3.
if (x - x//1) > (y - y//1):
return x
return y

---
Preconditions and postconditions
initial state S0
def grtfrac(x, y):
    if (x - x//1) > (y - y//1):
        return x
    else:
        return y
transitions S0 → S1, S2
true
false
S1
S2
transition S2 → S4
transition S1 → S3
final state S4
final state S3
S0: x and y are floating-point numbers (by contract!).
S1: x, y as above; the fractional part of x is greater than that of y.
S2: x, y as above; the fractional part of y is greater than that of x, or equal.
S3: The fractional part of x is the greater one, and x was returned.
S4: The fractional part of y is the greater one (or they are equal); y was returned.
if (x - x//1) > (y - y//1):
return x
return y

---
Problem: Matching natural numbers
def natmatch_iter(x, y):
    for i in range(len(x)):
        for j in range(i+1, len(x)):
        if (x[i]+x[j] == y) and (x[i] != x[j]):
        return [x[i], x[j]]
    return []
Examples:
If x is [17, 10, 4, 1] and y is 21, return any of [17, 4] or [4, 17].
If x is the same as above and y is 12, return the empty list [].
Specification
The function takes a list of natural numbers x as its first argument and a natural number y as its second argument. If in the list x, there are elements a and b which are not equal and add up to exactly y, the list [a, b] is returned; otherwise, [] is returned.

---
Problem: Matching natural numbers
def natmatch_recur_core(x, y, l):
    if 1 >= l:
        return []
    else:
        for i in range(l-1):
        if (x[i]+x[l-1] == y) and (x[i] != x[l-1]):
        return [x[i], x[l-1]]
        return natmatch_recur_core(x, y, l-1)
def natmatch_recur(x, y):
    return natmatch_recur_core(x, y, len(x))
def natmatch_iter(x, y):
    for i in range(len(x)):
        for j in range(i+1, len(x)):
        if (x[i]+x[j] == y) and (x[i] != x[j]):
        return [x[i], x[j]]
    return []
Specification
The function takes a list of natural numbers x as its first argument and a natural number y as its second argument. If in the list x, there are elements a and b which are not equal and add up to exactly y, the list [a, b] is returned; otherwise, [] is returned.

---
Verification of loop constructs
initial state S0
end
def natmatch_iter(x, y):
    for i in range(len(x)):
        for j in range(i+1, len(x)):
        if (x[i]+x[j] == y) and (x[i] != x[j]):
        return [x[i], x[j]]
    return []
S2
next
S1
final
state S3
for i in range(len(x)):
for j in range(i+1, len(x)):
return []
Specification
The function takes a list of natural numbers x as its first argument and a natural number y as its second argument. If in the list x, there are elements a and b which are not equal and add up to exactly y, the list [a, b] is returned; otherwise, [] is returned.

---
Verification of loop constructs
initial state S0
end
def natmatch_iter(x, y):
    for i in range(len(x)):
        for j in range(i+1, len(x)):
        if (x[i]+x[j] == y) and (x[i] != x[j]):
        return [x[i], x[j]]
    return []
S2
next
S5
S1
end
next
S4
final
state S3
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return []
Specification
The function takes a list of natural numbers x as its first argument and a natural number y as its second argument. If in the list x, there are elements a and b which are not equal and add up to exactly y, the list [a, b] is returned; otherwise, [] is returned.

---
Verification of loop constructs
initial state S0
end
def natmatch_iter(x, y):
    for i in range(len(x)):
        for j in range(i+1, len(x)):
        if (x[i]+x[j] == y) and (x[i] != x[j]):
        return [x[i], x[j]]
    return []
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []
Specification
The function takes a list x and a natural number y as arguments. If in the list x, there are elements a and b which are not equal and add up to y, the list [a, b] is returned; otherwise, [] is returned.

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1, first iteration: i ≡ 0, len(x) ≥ 1.
S4, first iteration: i ≡ 0, j ≡ 1, len(x) ≥ 2.
S8, first iteration: As above, and x[0] + x[1] do not match.
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1, first iteration: i ≡ 0, len(x) ≥ 1.
S4, first iteration: i ≡ 0, j ≡ 1, len(x) ≥ 2.
S8, first iteration: As above, and x[0] + x[1] do not match.
Task now: Find a loop invariant, one that holds every time that the execution states S4 and S8 inside the inner loop are visited.
(Still assuming that i remains 0.)
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1, first iteration: i ≡ 0, len(x) ≥ 1.
S4, invariant: i ≡ 0, 0 < j < len(x), and x[0] does not match with
any x[k] for indices k < j.
S8, invariant: As above, but
x[0] does not match with any
x[k] for indices k ≤ j.
(Still assuming that i remains 0.)
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1, first iteration: i ≡ 0, len(x) ≥ 1.
S4, invariant: i ≡ 0, 0 < j < len(x), and x[0] does not match with
any x[k] for indices k < j.
S8, invariant: As above, but
x[0] does not match with any
x[k] for indices k ≤ j.
(Still assuming that i remains 0.)
S2
next
S5
S1
end
next
Remark
This proof technique is called mathematical induction:
We know that it is true for the base case (j = 0).
We know that if it is true for j, it is also true for j+1.
Therefore it is true for all j.
We did this for the inner loop, still assuming that the outer loop is in its first iteration (i = 0). Now we apply the same technique there.
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1, for i ≡ 0: i ≡ 0, len(x) ≥ 1.
S4, for i ≡ 0: i ≡ 0, 0 < j < len(x), and x[0] does not match with
any x[k] for indices k < j.
S8, for i ≡ 0: As above, but
x[0] does not match with any
x[k] for indices k ≤ j.
S5, for i ≡ 0: i ≡ 0, and after trying all indices 0 < j < len(x), x[0] was not found to match any.
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1, invariant: 0 ≤ i < len(x).
S4, invariant: 0 ≤ i < len(x),
i < j < len(x), all indices smaller than i did not yield a match,
and x[i] does not match with
any x[k] for indices i < k < j.
S8, invariant: As above, and
x[i] does not match with any
x[k] for indices i < k ≤ j.
S5, invariant: As above, and we now know that x[i] does not yield a match with any other element.
(And neither did any smaller i.)
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1: 0 ≤ i < len(x).
S5: No combination of any x[i]
that was tried so far, with any
x[j] from the list where i < j,
produces a valid match.
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Verification of loop constructs
initial state S0
end
S0: x and y given as specified.
S1: 0 ≤ i < len(x).
S5: No combination of any x[i]
that was tried so far, with any
x[j] from the list where i < j,
produces a valid match.
S6: x[i] and x[j] are a match.
S7: Match found and returned.
S2: End of list, all pairs of ele-
ments were tried, none matched.
S3: No match; [] was returned.
S2
next
S5
S1
end
next
S8
S4
false
true
final state S3
S6
final state S7
for i in range(len(x)):
for j in range(i+1, len(x)):
if (x[i]+x[j] == y) and (x[i] != x[j]):
return [x[i], x[j]]
return []

---
Performance and
efficiency

---
Levels of abstraction in program analysis
Binary executable (equivalently, script + executable interpreter)
Program implementation (code)
Algorithm description (pseudocode)
Problem statement
performance, i.e., resource requirements, on given hardware
influenced by compiler/interpreter choice and configuration, etc.
accessible to automated analysis; formal verification may be possible
different programming languages entail variation in data structures, etc.
accessible to analysis by humans; e.g., efficiency of the algorithm
informal representation, independent of implementation and architecture
open to theoretical investigation; complexity: best possible efficiency
proofs of upper or lower bounds apply to any potential algorithm

---
Performance as a function of the problem size
Usually we are not interested in the resource requirements of a single execution, but in understanding how the requirements behave as a function of a charac-
teristic quantity, the problem size n, that describes the magnitude of the task.
We distinguish between:
Time requirements, describing the computing time. Where possible, this should be expressed in terms of actual CPU time (+ I/O time); the opera-
ting system will usually distribute CPU time between multiple processes.
Memory (or space) requirements, describing the memory allocated to the program; depending on definition, this may include I/O size.

---
Performance as a function of the problem size
Usually we are not interested in the resource requirements of a single execution, but in understanding how the requirements behave as a function of a charac-
teristic quantity, the problem size n, that describes the magnitude of the task.
We distinguish between:
Time requirements, describing the computing time. Where possible, this should be expressed in terms of actual CPU time (+ I/O time); the opera-
ting system will usually distribute CPU time between multiple processes.
Memory (or space) requirements, describing the memory allocated to the program; depending on definition, this may include I/O size.
Worst-case performance, which for any given problem size n corres-
ponds to the input/special case of size n with the greatest requirements.
Average-case performance, over many representative cases of size n.
There is also “best-case performance,” but usually not as an evaluation criterion.

---
Algorithm efficiency as a function of problem size
Usually we are not interested in the efficiency of an algorithm for a single input value, but in understanding how the efficiency behaves as a function of a charac-
teristic quantity, the problem size n, that describes the magnitude of the task.
We distinguish between:
Time efficiency measure(s), describing CPU time in an abstract way; one possible measure for it is the number of code/pseudocode instructions.
Space or memory efficiency measure(s), describing the memory in an abstract way, e.g., by the number of elementary values stored in varia-
bles, data structures, or files; this usually excludes the initial input.
Worst-case efficiency, which for any given problem size n corresponds to the special case of size n with the greatest computing time/memory.
Average-case efficiency, over all (or many representative) cases of size n.
There is also “best-case efficiency,” but usually not as an evaluation criterion.

---
Algorithm efficiency as a function of problem size
Usually we are not interested in the efficiency of an algorithm for a single input value, but in understanding how the efficiency behaves as a function of a charac-
teristic quantity, the problem size n, that describes the magnitude of the task.
We distinguish between:
Time efficiency measure(s), describing CPU time in an abstract way; one possible measure for it is the number of code/pseudocode instructions.
Space or memory efficiency measure(s), describing the memory in an abstract way, e.g., by the number of elementary values stored in varia-
bles, data structures, or files; this usually excludes the initial input.
Observation
Performance analysis is carried out by measurements; it is usually very hard to determine the worst case, therefore it is common to describe the average-case performance, e.g., from random input.
Algorithm efficiency can consider both the average and the worst case, but the average case usually requires a statistical analysis. Statements on the worst case can be very straightforward.
Worst-case efficiency, which for any given problem size n corresponds to the special case of size n with the greatest computing time/memory.
Average-case efficiency, over all (or many representative) cases of size n.
There is also “best-case efficiency,” but usually not as an evaluation criterion.

---
Example: Fibonacci sequence
recursive code
(with store-and-recall)
iterative code

---
Example: Number matching
recursive code
iterative code

---
Asymptotic efficiency (or performance)
Often we are most interested in the qualitative scaling behaviour of algorithms.
For this purpose, Landau notation is used,1 also known as “big O notation.” For any given efficiency or requirements measure, this is obtained as follows:
Eliminate all except the leading contribution, i.e., the one that dominates the measure for large values of n. It is the one that grows fastest:
From 3n3 + 12n + 17, we retain only 3n3.
From 16·2n + 5n3, we retain only 16·2n.
If you are unsure, insert n = 1000 and see which term is greatest.
Eliminate constant coefficients; 3n3 becomes O(n3), 16·2n becomes O(2n).
1Named for Edmund Landau (1877 – 1938) who developed this notation for infinitesimal calculus.

---
Asymptotic efficiency (or performance)
Often we are most interested in the qualitative scaling behaviour of algorithms.
For this purpose, Landau notation is used,1 also known as “big O notation.” For any given efficiency or requirements measure, this is obtained as follows:
Eliminate all except the leading contribution, i.e., the one that dominates the measure for large values of n. It is the one that grows fastest:
From 3n3 + 12n + 17, we retain only 3n3.
From 16·2n + 5n3, we retain only 16·2n.
If you are unsure, insert n = 1000 and see which term is greatest.
Eliminate constant coefficients; 3n3 becomes O(n3), 16·2n becomes O(2n).
If an algorithm includes 3n3 + 12n + 17 instructions in the worst case, we can say, it is in time efficiency class O(n3), or simply, it has time efficiency O(n3).
1Named for Edmund Landau (1877 – 1938) who developed this notation for infinitesimal calculus.

---
CO2412
Computational Thinking
Formal verification
Performance and efficiency